## Slide 1
Date | Day | Class No. | Title | Chapters | HW Due date | Lab Due date | Exam
1 Sept | Mon |  | Labor Day |  |  | NO LAB | 
2 Sept | Tue |  |  |  |  | NO LAB | 
3 Sept | Wed | 1 | Fundamentals | 2.1 |  |  | 
4 Sept | Thu |  |  |  |  |  | 
5 Sept | Fri |  | NO Recitation |  |  |  | 
6 Sept | Sat |  |  |  |  |  | 
7 Sept | Sun |  |  |  |  |  | 
8 Sept | Mon | 2 | Kirchoff’s Laws | 2.2 – 2.3 |  | NO LAB | 
9 Sept | Tue |  |  |  |  | NO LAB | 
Schedule…

## Slide 2: Small and Simple
Alma 37:6
6 Now ye may suppose that this is foolishness in me; but behold I say unto you, that by small and simple things are great things brought to pass; and small means in many instances doth confound the wise.

## Slide 3: Lecture 1 – Fundamentals of Electrical Circuits

## Slide 4: Important Concepts
Ideal/Dependent voltage sources
Ideal/Dependent current sources
Electrical Networks
  Branches
  Nodes
  Loops
  Meshes

## Slide 5: Ideal Voltage Sources
An electric device that generates a prescribed voltage
Provides a prescribed voltage across its terminals irrespective of the current flowing through it. The amount of current supplied by the source is determined by the circuit connected to it

## Slide 6: Ideal Voltage Sources
Time-dependent voltage source
  Voltage as a function of time t
  Lowercase v usually connotes AC source
+
_
vs(t)
vs(t)
+
_
i
Circuit

## Slide 7: Ideal Voltage Sources
Time-dependent voltage source – special case: sinusoidal
  Voltage as a function of time t
    IE: vs(t) = Vcos(ωt)
  Lowercase v usually connotes AC source
+
_
vs(t)
vs(t)
+
_
~
i
Circuit

## Slide 8: Ideal Voltage Sources
DC voltage source
  Voltage is not a function of time
  Capital V connotes DC voltage
  DC voltage source example: a battery
v
+
_
+
_
Vs
i
Circuit
A generic voltage is denoted by just a lowercase v

## Slide 9: Ideal Voltage Sources
Source-load representation
+ -
Battery
Light
Vs
+
_
v
+
_
i
R
v
+
_
i
Source
Load

## Slide 10: Ideal Current Sources
An electric device that generates a prescribed current
Provides a prescribed current to any circuit connected to it. The voltage generated by the source is determined by the circuit connected to it.

## Slide 11: Ideal Current Sources
Lowercase i connotes AC current
Capital I connotes DC current
is,Is
vs
+
_
is, Is
Circuit

## Slide 12: Dependent (Controlled) Sources
Diamond shaped source indicates dependent source
Dependent sources are an important part of amplifiers
Source Type | Relationship
Voltage controlled voltage source (VCVS) | vs = avx
Current controlled voltage source (CCVS) | vs = aix
Voltage controlled current source (VCCS) | is = avx
Current controlled current source (CCCS) | is = aix
+
_
vs
is

## Slide 13: Electrical Network
A collection of elements through which current flows
Vs1
+
_
Vs2
+
_
R1
R2
R3
R4
R5

## Slide 14: Electrical Network - Branches
Any portion of a circuit with two terminals connected to it.
May consist of one or more circuit elements
Vs1
+
_
Vs2
+
_
R1
R2
R3
R4
R5
+
_
i
v
Branch
voltage
Branch
current

## Slide 15: Electrical Network - Branches
Any portion of a circuit with two terminals connected to it.
May consist of one or more circuit elements
Vs1
+
_
Vs2
+
_
R1
R2
R3
R4
R5
+
_
i
v
Branch
voltage
Branch
current

## Slide 16: Electrical Network - Nodes
The junction of two or more branches
Trivial Node: the junction of only two branches
R1
Vs1
+
_
Vs2
+
_
R2
R3
R4
R5
Node

## Slide 17: Electrical Network - Nodes
The junction of two or more branches
Trivial Node: the junction of only two branches
R1
Vs1
+
_
Vs2
+
_
R2
R3
R4
R5
Node
Node b
Node a
Node c

## Slide 18: Electrical Network – Supernodes
Obtained by defining a region that encloses more than one node
Can be treated the exact same way as normal nodes
Vs1
+
_
Vs2
+
_
R2
R3
R4
R5
Supernode
R1

## Slide 19: Electrical Network – Loops
Any enclosed connection of branches
Vs1
+
_
Vs2
+
_
R2
R3
R4
R5
R1

## Slide 20: Electrical Network – Meshes
A loop that does not contain other loops
Vs1
+
_
Vs2
+
_
R2
R3
R4
R5
R1