## Slide 1
Date | Day | Class No. | Title | Chapters | HW Due date | Lab Due date | Exam
8 Oct | Wed | 11 | Dynamic Circuits | 4.2 – 4.4 |  |  | 
9 Oct | Thu |  |  |  |  |  | 
10 Oct | Fri |  | Recitation |  | HW 5 |  | 
11 Oct | Sat |  |  |  |  |  | 
12 Oct | Sun |  |  |  |  |  | 
13 Oct | Mon | 12 | Exam 1 Review |  |  | LAB 4 | EXAM 1
14 Oct | Tue |  |  |  |  |  | 
15 Oct | Wed | 13 | AC Circuit Analysis | 4.5 |  |  | 
Schedule…

## Slide 2: Change
1 Corinthians 15:51-57
51 Behold, I shew you a mystery; We shall not all sleep, but we shall all be changed,
52 In a moment, in the twinkling of an eye, at the last trump: for the trumpet shall sound, and the dead shall be raised incorruptible, and we shall be changed.
53 For this corruptible must put on incorruption, and this mortal must put on immortality.
54 So when this corruptible shall have put on incorruption, and this mortal shall have put on immortality, then shall be brought to pass the saying that is written, Death is swallowed up in victory.
55 O death, where is thy sting? O grave, where is thy victory?
56 The sting of death is sin; and the strength of sin is the law.
57 But thanks be to God, which giveth us the victory through our Lord Jesus Christ.

## Slide 3: Lecture 11 – Dynamic Circuits
Time-Dependent Sources

## Slide 4: Time Dependent Sources
Periodic signals: repeating patterns that appear frequently in practical applications
  A periodic signal x(t) satisfies the equation:

## Slide 5: Time Dependent Sources
Sinusoidal signal: a periodic waveform satisfying the following equation:
A – amplitude
ω – radian frequency
φ – phase
A
-A
T
φ/ω

## Slide 6: Sinusoidal Sources
Helpful identities:

## Slide 7: Sinusoidal Sources
Why sinusoidal sources?
Sinusoidal AC is the fundamental current type supplied to homes throughout the world by way of power grids
  Current war:
    late 1880’s AC (Westinghouse and Tesla) competed with DC (Edison) for the electric power grid standard
    Low frequency AC (50 - 60Hz) can be more dangerous than DC
      Alternating fluctuations can cause the heart to lose coordination (death)
    High frequency DC can be more dangerous than AC
      causes muscles to lock in position – preventing victim from releasing conductor
    DC has serious limitations
      DC cannot be transmitted over long distances (greater than 1 mile) without serious power losses
      DC cannot be easily changed to higher or lower voltages

## Slide 8: Measuring Signal Strength
Methods of quantifying the strength of time-varying electric signals:
  Average (DC) value
    Mean voltage (or current) over a period of time
  Root-mean-square (RMS) value
    Takes into account the fluctuations of the signal about its average value

## Slide 9: Measuring Signal Strength
Time – averaged signal strength: integrate signal x(t) over a period (T) of time

## Slide 10: Measuring Signal Strength
Example1: compute the average value of the signal – x(t) = 10cos(100t)

## Slide 11: Measuring Signal Strength
Example1: compute the average value of the signal – x(t) = 10cos(100t)

## Slide 12: Measuring Signal Strength
Example1: compute the average value of the signal – x(t) = 10cos(100t)
NB: in general, for any sinusoidal signal

## Slide 13: Measuring Signal Strength
Root–mean–square (RMS): since a zero average signal strength is not useful, often the RMS value is used instead
  The RMS value of a signal x(t) is defined as:
NB: the rms value is simply the square root of the average (mean) after being squared – hence: root – mean – square
NB: often notation is used instead of

## Slide 14: Measuring Signal Strength
Example2: Compute the rms value of the sinusoidal current i(t) = I cos(ωt)

## Slide 15: Measuring Signal Strength
Example2: Compute the rms value of the sinusoidal current i(t) = I cos(ωt)
Integrating a sinusoidal waveform over 2 periods equals zero

## Slide 16: Measuring Signal Strength
Example2: Compute the rms value of the sinusoidal current i(t) = I cos(ωt)
The RMS value of any sinusoid signal is always equal to 0.707 times the peak value (regardless of amplitude or frequency)

## Slide 17: Network Analysis with Capacitors and Inductors (Dynamic Circuits)
Differential Equations

## Slide 18: Dynamic Circuit Network Analysis
Kirchoff’s law’s (KCL and KVL) still apply, but they will now produce differential equations.
+ R –
iR
+
C
–
iC
vs(t)
+
–
~

## Slide 19: Dynamic Circuit Network Analysis
Kirchoff’s law’s (KCL and KVL) still apply, but they will now produce differential equations.
+ R –
iR
+
C
–
iC
vs(t)
+
–
~

## Slide 20: Dynamic Circuit Network Analysis
Kirchoff’s law’s (KCL and KVL) still apply, but they will now produce differential equations.
+ R –
iR
+
C
–
iC
vs(t)
+
–
~

## Slide 21: Sinusoidal Source Responses
Consider the AC source producing the voltage:
vs(t) = Vcos(ωt)
+ R –
iR
+
C
–
iC
vs(t)
+
–
~
The solution to this diff EQ will be a sinusoid:

## Slide 22: Sinusoidal Source Responses
Consider the AC source producing the voltage:
vs(t) = Vcos(ωt)
+ R –
iR
+
C
–
iC
vs(t)
+
–
~
Substitute the solution form into the diff EQ:

## Slide 23: Sinusoidal Source Responses
Consider the AC source producing the voltage:
vs(t) = Vcos(ωt)
+ R –
iR
+
C
–
iC
vs(t)
+
–
~
For this equation to hold, both the sin(ωt) and cos(ωt) coefficients must be zero

## Slide 24: Sinusoidal Source Responses
Consider the AC source producing the voltage:
vs(t) = Vcos(ωt)
+ R –
iR
+
C
–
iC
vs(t)
+
–
~
Solving these equations for A and B gives:

## Slide 25: Sinusoidal Source Responses
Consider the AC source producing the voltage:
vs(t) = Vcos(ωt)
+ R –
iR
+
C
–
iC
vs(t)
+
–
~
Writing the solution for vC(t):
NB: This is the solution for a single-order diff EQ (i.e. with only one capacitor)

## Slide 26: Sinusoidal Source Responses
vc(t) has the same frequency, but different amplitude and different phase than vs(t)
vs(t)
vc(t)
What happens when R or C is small?

## Slide 27: Sinusoidal Source Responses
In a circuit with an AC source: all branch voltages and currents are also sinusoids with the same frequency as the source. The amplitudes of the branch voltages and currents are scaled versions of the source amplitude (i.e. not as large as the source) and the branch voltages and currents may be shifted in phase with respect to the source.
+ R –
iR
+
C
–
iC
vs(t)
+
–
~
3 parameters that uniquely identify a sinusoid:
  frequency
  amplitude
  phase