## Slide 1
Date | Day | Class No. | Title | Chapters | HW Due date | Lab Due date | Exam
8 Sept | Mon | 2 | Kirchoff’s Laws | 2.2 – 2.3 |  | NO LAB | 
9 Sept | Tue |  |  |  |  | NO LAB | 
10 Sept | Wed | 3 | Power | 2.4 – 2.5 |  |  | 
11 Sept | Thu |  |  |  |  | NO LAB | 
12 Sept | Fri |  | Recitation |  | HW 1 |  | 
13 Sept | Sat |  |  |  |  |  | 
14 Sept | Sun |  |  |  |  |  | 
15 Sept | Mon | 4 | Ohm’s Law | 2.5 – 2.6 |  | LAB 1 | 
16 Sept | Tue |  |  |  |  |  | 
Schedule…

## Slide 2: Divine Source
2 Nephi 25:26
26 And we talk of Christ, we rejoice in Christ, we preach of Christ, we prophesy of Christ, and we write according to our prophecies, that our children may know to what source they may look for a remission of their sins.

## Slide 3: Lecture 2 – Kirchhoff’s Current and Voltage Laws

## Slide 4: Charge
Elektron: Greek word for amber
  ~600 B.C. it was discovered that static charge on a piece of amber could attract light objects (feathers)
Charge (q): fundamental electric quantity
  Smallest amount of charge is that carried by an electron/proton (elementary charges):
Coulomb (C): basic unit of charge.

## Slide 5: Electric Current
Electric current (i): the rate of change (in time) of charge passing through a predetermined area (IE the cross-sectional area of a wire).
  Analogous to volume flow rate in hydraulics
  Current (i) refers to ∆q (dq) units of charge that flow through a cross-sectional area (Area) in ∆t (dt) units of time
i
Area
Ampere (A): electric current unit.
1 ampere = 1 coulomb/second (C/s)
Positive current flow is in the direction of positive charges (the opposite direction of the actual electron movement)

## Slide 6: Charge and Current Example
For a metal wire, find:
  The total charge (q)
  The current flowing in the wire (i)
Given Data:
  wire length = 1m
  wire diameter = 2 x 10-3m
  charge density = n = 1029 carriers/m3
  charge of an electron = qe = -1.602 x 10-19
  charge carrier velocity = u = 19.9 x 10-6 m/s

## Slide 7: Charge and Current Example
For a metal wire, find:
  The total charge (q)
  The current flowing in the wire (i)
Given Data:
  wire length = 1m
  wire diameter = 2 x 10-3m
  charge density = n = 1029 carriers/m3
  charge of an electron = qe = -1.602 x 10-19
  charge carrier velocity = u = 19.9 x 10-6 m/s

## Slide 8: Charge and Current Example
For a metal wire, find:
  The total charge (q)
  The current flowing in the wire (i)
Given Data:
  wire length = 1m
  wire diameter = 2 x 10-3m
  charge density = n = 1029 carriers/m3
  charge of an electron = qe = -1.602 x 10-19
  charge carrier velocity = u = 19.9 x 10-6 m/s

## Slide 9: Charge and Current Example
For a metal wire, find:
  The total charge (q)
  The current flowing in the wire (i)
Given Data:
  wire length = 1m
  wire diameter = 2 x 10-3m
  charge density = n = 1029 carriers/m3
  charge of an electron = qe = -1.602 x 10-19
  charge carrier velocity = u = 19.9 x 10-6 m/s

## Slide 10: Kirchhoff’s Current Law (KCL)
KCL: charge must be conserved – the sum of the currents at a node must equal zero.
+
_
1.5 V
i
i
i1
i2
i3
Node 1
At Node 1:
-i + i1 + i2 + i3 = 0
OR:
i - i1 - i2 - i3 = 0
NB: a circuit must be CLOSED in order for current to flow

## Slide 11: Kirchhoff’s Current Law (KCL)
Potential problem of too many branches on a single node:
  not enough current getting to a branch
Suppose:
  all lights have the same resistance
  i4 needs 1A
What must the value of i be?
+
_
1.5 V
i
i
i1
i2
i6
i3
i4
i5
Node 1

## Slide 12: Kirchhoff’s Current Law (KCL)
Potential problem of too many branches on a single node:
  not enough current getting to a branch
-i + i1 + i2 + i3 + i4 + i5 + i6 = 0
BUT: since all resistances are the same:
i1 = i2 = i3 = i4 = i5 = i6 = in
-i + 6in = 0
6in = i
6(1A) = i
i = 6A
+
_
1.5 V
i
i
i1
i2
i6
i3
i4
i5
Node 1

## Slide 13: Kirchhoff’s Current Law (KCL)
Example1: find i0 and i4
  is = 5A, i1 = 2A, i2 = -3A, i3 = 1.5A
+
_
Vs
is
i0
i1
i2
i3
i4

## Slide 14: Kirchhoff’s Current Law (KCL)
Example1: find i0 and i4
  is = 5A, i1 = 2A, i2 = -3A, i3 = 1.5A
+
_
Vs
is
i0
i1
i2
i3
i4
Node a
Node c
Node b
NB: First thing to do – decide on unknown current directions.
  If you select the wrong direction it won’t matter
    a negative current indicates current is flowing in the opposite direction.
  Must be consistent
    Once a current direction is chosen must keep it

## Slide 15: Kirchhoff’s Current Law (KCL)
Example1: find i0 and i4
  is = 5A, i1 = 2A, i2 = -3A, i3 = 1.5A
+
_
Vs
is
i0
i1
i2
i3
i4
Node a
Node c
Node b

## Slide 16: Kirchhoff’s Current Law (KCL)
Example2: using KCL find is1 and is2
  i3 = 2A, i5 = 0A, i2 = 3A, i4 = 1A
Vs1
+
_
Vs2
+
_
R2
R3
R4
R5
is1
i2
is2
i4
i3
i5

## Slide 17: Kirchhoff’s Current Law (KCL)
Example2: using KCL find is1 and is2
  i3 = 2A, i5 = 0A, i2 = 3A, i4 = 1A
Vs1
+
_
Vs2
+
_
R2
R3
R4
R5
Supernode
is1
i2
is2
i4
i3
i5

## Slide 18: Kirchhoff’s Current Law (KCL)
Vs1
+
_
Vs2
+
_
R2
R3
R4
R5
is1
i2
is2
i4
i3
i5
Node a
Example2: using KCL find is1 and is2
  i3 = 2A, i5 = 0A, i2 = 3A, i4 = 1A

## Slide 19: Voltage
Moving charges in order to produce a current requires work
Voltage: the work (energy) required to move a unit charge between two points
Volt (V): the basic unit of voltage (named after Alessandro Volta)
Volt (V): voltage unit.
1 Volt = 1 joule/coulomb (J/C)

## Slide 20: Voltage
Voltage is also called potential difference
  Very similar to gravitational potential energy
  Voltages are relative
    voltage at one node is measured relative to the voltage at another node
    Convenient to set the reference voltage to be zero
+
vab
_
a
b
_
+
vba
vab => the work required to move a positive charge from terminal a to terminal b
vba => the work required to move a positive charge from terminal b to terminal a
vba = - vab
vab = va - vb

## Slide 21: Voltage
Polarity of voltage direction (for a given current direction) indicates whether energy is being absorbed or supplied
+
vab
_
a
b
i
vba
_
a
b
i
+
Since i is going from + to – energy is being absorbed by the element (passive element)
Since i is going from – to + energy is being supplied by the element (active element)

## Slide 22: Voltage
Polarity of voltage direction (for a given current direction) indicates whether energy is being absorbed or supplied
+
vab
_
a
b
i
vba
_
a
b
i
+
+
_
1.5 V
i
i
v1
a
b
vab
+
+
_
_
Supplying energy
(source)
(active element)
NEGATIVE voltage
Absorbing energy
(load)
(passive element)
POSITIVE voltage

## Slide 23: Voltage
Work (W) done in moving a charge q across terminals a and b:
+
vab
_
a
b
i
+
_
1.5 V
v1
a
b
+
_

## Slide 24: Voltage
Ground: represents a specific reference voltage
  Most often ground is physically connected to the earth (the ground)
  Convenient to assign a voltage of 0V to ground
The ground symbol we’ll use
(earth ground)
Another ground symbol
(chasis ground)

## Slide 25: Kirchhoff’s Voltage Law (KVL)
KVL: energy must be conserved – the sum of the voltages in a closed circuit must equal zero.
+
_
1.5 V
i
i
v1
a
b
vab
+
+
_
_
Use Node b as the reference voltage (ground): vb = 0

## Slide 26: Kirchhoff’s Voltage Law (KVL)
Example3: using KVL, find v2
  vs1 = 12V, v1 = 6V, v3 = 1V
Vs1
+
_
i
+ v1 –
+
v3
–
+ v2 –
Source: loop travels from – to + terminals
  Sources have negative voltage
Load: loop travels from + to – terminals
  Loads have positive voltage

## Slide 27: Kirchhoff’s Voltage Law (KVL)
Example3: using KVL, find v2
  vs1 = 12V, v1 = 6V, v3 = 1V
Vs1
+
_
i
+ v1 –
+
v3
–
+ v2 –
Source: loop travels from – to + terminals
  Sources have negative voltage
Load: loop travels from + to – terminals
  Loads have positive voltage

## Slide 28: Kirchhoff’s Voltage Law (KVL)
Example3: using KVL, find v2
  vs1 = 12V, v1 = 6V, v3 = 1V
Vs1
+
_
i
+ v1 –
+
v3
–
+ v2 –
NB: v2 is the voltage across two elements in parallel branches.
The voltage across both elements is the same: v2

## Slide 29: Kirchhoff’s Voltage Law (KVL)
Example4: using KVL find v1 and v4
  vs1 = 12V, vs2 = -4V, v2 = 2V, v3 = 6V, v5 = 12V
Vs1
+
_
Vs2
+
_
+
v3
–
+ v4 –
+ v1 –
+
v5
–
+
v2
–

## Slide 30: Kirchhoff’s Voltage Law (KVL)
Example4: using KVL find v1 and v4
  vs1 = 12V, vs2 = -4V, v2 = 2V, v3 = 6V, v5 = 12V
Vs1
+
_
Vs2
+
_
+
v3
–
+ v4 –
+ v1 –
+
v5
–
+
v2
–
Loop1
Loop2
Loop3

## Slide 31: Kirchhoff’s Voltage Law (KVL)
Example4: using KVL find v1 and v4
  vs1 = 12V, vs2 = -4V, v2 = 2V, v3 = 6V, v5 = 12V
Vs1
+
_
Vs2
+
_
+
v3
–
+ v4 –
+ v1 –
+
v5
–
+
v2
–
Loop1
Loop2
Loop3

## Slide 32: Kirchhoff’s Voltage Law (KVL)
Example4: using KVL find v1 and v4
  vs1 = 12V, vs2 = -4V, v2 = 2V, v3 = 6V, v5 = 12V
Vs1
+
_
Vs2
+
_
+
v3
–
+ v4 –
+ v1 –
+
v5
–
+
v2
–
Loop1
Loop2
Loop3