## Slide 1
Date | Day | Class No. | Title | Chapters | HW Due date | Lab Due date | Exam
19 Nov | Wed | 23 | Sequential Logic | 14.1 |  |  | 
20 Nov | Thu |  |  |  |  |  | 
21 Nov | Fri |  | Recitation |  | HW 9 |  | 
22 Nov | Sat |  |  |  |  |  | 
23 Nov | Sun |  |  |  |  |  | 
24 Nov | Mon | 24 | DAC | 15.4 |  |  | 
25 Nov | Tue |  | Recitation |  | HW 10 |  | 
26 Nov | Wed |  | Thanksgiving |  |  |  | 
Schedule…

## Slide 2: Memory & Counters
Exodus 12:14
14 And this day shall be unto you for a memorial; and ye shall keep it a feast to the LORD throughout your generations; ye shall keep it a feast by an ordinance for ever.
D&C 107:100
100 He that is slothful shall not be counted worthy to stand, and he that learns not his duty and shows himself not approved shall not be counted worthy to stand. Even so. Amen.

## Slide 3: Lecture 23 – Combinational & Sequential Logic

## Slide 4: Digital Logic Hierarchy
2To4
FA
D
Mem
n
m
m
Intel
Sequential
Combinational
Gates
Transistors
Processors

## Slide 5: Combinational Logic
Decoders
Multiplexers

## Slide 6: Decoders
Decode the input and signify its value by raising just one of its outputs.
A decoder with n inputs has 2n outputs
X
Y
Z
W
2-to-4
Decoder
A
B
W
X
Y
Z
DECODER Symbol

## Slide 7: Decoders
Write the truth table
X
Y
Z
W

## Slide 8: Decoders
Write the truth table
X
Y
Z
W
A | B | W | X | Y | Z
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1

## Slide 9: Multiplexors
Connect one of its inputs to its output according to select signals
Useful for selecting one from a collection of data inputs.
Usually has 2n inputs and n select lines.
A
B
S
C
1
0
MULTIPLEXOR Symbol

## Slide 10: Multiplexors
Write the truth table
A
B
S
C
1
0
MULTIPLEXOR Symbol
A | B | S | C
0 | 0 | 0 | ?
0 | 0 | 1 | ?
0 | 1 | 0 | ?
0 | 1 | 1 | ?
1 | 0 | 0 | ?
1 | 0 | 1 | ?
1 | 1 | 0 | ?
1 | 1 | 1 | ?

## Slide 11: Multiplexors
Write the truth table
A
B
S
C
1
0
MULTIPLEXOR Symbol
A | B | S | C
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1

## Slide 12: Sequential Logic

## Slide 13: Latches and Flip-Flops (FFs)
Latch/FF: basic building block of memory devices
  Bistable devices – remain in one of 2 states (logic 0 or logic 1)
  Has 2 outputs (one is the complement of the other) – often only one is shown (the other is implied)
Latches – imply that not controlled by a clock
FFs – imply that they are controlled by a clock
D
Q
CLK
T
Q
CLK
J
Q
CLK
K
D - FF
JK - FF
T - FF
S
Q
R
D
Q
E
S
Q
R
E
D – Latch
with enable
SR – Latch
with enable
SR – Latch

## Slide 14: SR Latch
SR Latch has 3 allowed states:
  Set (set Q to 1): S = 1, R = 0
  Reset (reset Q to 0): R = 1, S = 0
  Present state (keep Q as is): S = 0, R = 0
SR Latch has 1 illegal state:
  Instability (causes Q to switch between 0 and 1): S = 1, R = 1
S
R
Q
Q
S
Q
R
S | R | Qnew
0 | 0 | Qold
0 | 1 | 0
1 | 0 | 1
1 | 1 | X
Present state
Reset
Set
Illegal

## Slide 15: SR Latch
Timing diagram: a graph of inputs and outputs over time.
Time
S
R
Q
FF is set
FF is reset
FF is again reset
FF is set
HOLD
HOLD
HOLD
HOLD
S | R | Qnew
0 | 0 | Qold
0 | 1 | 0
1 | 0 | 1
1 | 1 | X

## Slide 16: SR Latch
SR Latch with additional inputs:
  Enable (E) – S and R can only change Q when E is 1
  Preset (PRE) – regardless of S, R, or E, put Q to 1 when PRE is 1
  Clear (CLR) – regardless of S, R, E, or PRE, put Q to 0 when CLR is 1
S
Q
R
E
PRE
CLR
E
S
R
PRE
CLR
Q
Precedence:
If CLR = 1, Q = 0
If PRE = 1, Q = 1
If E = 1, Q is set based on SR
  If S = 0 and R = 0, Q = hold
  If S = 0 and R = 1, Q = 0
  If S = 1 and R = 0, Q = 1
  If S = 1 and R = 1, Q = unstable
Else Q is held
SR can only change Q only in blue regions (where E = 1)

## Slide 17: D Latch
D Latch has only 2 states:
  Set (set Q to 1): D = 1
  Reset (reset Q to 0): D = 0
D Latch with enable (E):
  Q can only change when E = 1
E | D | Qnew
0 | 0 | Qold
0 | 1 | Qold
1 | 0 | 0
1 | 1 | 1
D
Q
E
S
Q
R
E
D
E
E
D
Q
D can only change Q only in blue regions (where E = 1)

## Slide 18: D Flip-Flop
D FF: 2 SR latches in master/slave configuration. The output (Q) changes on the rising clock edge
D | CLK | Qnew
0 |  | 0
1 |  | 1
D
Q
CLK
S
Q
R
S
Q
R
Q
E
E
CLK
D
Q
Master
Slave
CLK
D
Q
D can only change Q only on rising clock edge (arrows)
“Edge-Triggered”

## Slide 19: JK Flip-Flop
JK FF: 2 SR latches in master/slave configuration. The output (Q) changes on the falling clock edge
J | K | CLK | Qnew
0 | 0 |  | Qold
0 | 1 |  | 0
1 | 0 |  | 1
1 | 1 |  | Qold
JK FF has 4 allowed states:
  Present state (keep Q as is): J = 0, K = 0
  Reset (reset Q to 0): J = 0, K = 1
  Set (set Q to 1): J = 1, K = 0
  Toggle (set Q to Q): J = 1, K = 1
S
Q
R
S
Q
R
Q
E
E
CLK
J
Q
Q
K
J
Q
CLK
K
Indicates falling clock edge

## Slide 20: T Flip-Flop
T FF: JK FF with J and K inputs connected
T | CLK | Qnew
0 |  | Qold
1 |  | Qold
T FF has 2 allowed states:
  Present state (keep Q as is): T = 0
  Toggle (set Q to Q): T = 1
CLK
T
Q
J
Q
CLK
K
T
Q
CLK

## Slide 21: Flip-Flops
Example: Assuming the outputs of the following circuit start in a 000 state, determine the outputs for 4 clock cycles
CLK
T
Q
CLK
J
Q
CLK
K
D
Q
CLK
Q2
Q1
Q0

## Slide 22: Flip-Flops
Example: Assuming the outputs of the following circuit start in a 000 state, determine the outputs for 4 clock cycles
CLK
T | CLK | Qnew
0 |  | Qold
1 |  | Qold
D | CLK | Qnew
0 |  | 0
1 |  | 1
J | K | CLK | Qnew
0 | 0 |  | Qold
0 | 1 |  | 0
1 | 0 |  | 1
1 | 1 |  | Qold
0
0
0
0
0
0
0
1
1
1
0
Set outputs to 000
Based on output values change FF inputs
On each clock cycle:
  change FF outputs based on inputs
  Change FF inputs based on new outputs
T
Q
CLK
J
Q
CLK
K
D
Q
CLK
Q2
Q1
Q0

## Slide 23: Flip-Flops
Example: Assuming the outputs of the following circuit start in a 000 state, determine the outputs for 4 clock cycles
CLK
Cycle | Q2 | Q1 | Q0
start | 0 | 0 | 0
T | CLK | Qnew
0 |  | Qold
1 |  | Qold
D | CLK | Qnew
0 |  | 0
1 |  | 1
J | K | CLK | Qnew
0 | 0 |  | Qold
0 | 1 |  | 0
1 | 0 |  | 1
1 | 1 |  | Qold
0
0
0
0
0
0
0
1
1
1
0
Inputs changed due to outputs
T
Q
CLK
J
Q
CLK
K
D
Q
CLK
Q2
Q1
Q0

## Slide 24: Flip-Flops
Example: Assuming the outputs of the following circuit start in a 000 state, determine the outputs for 4 clock cycles
CLK
Cycle | Q2 | Q1 | Q0
start | 0 | 0 | 0
1 | 1 | 1 | 1
T | CLK | Qnew
0 |  | Qold
1 |  | Qold
D | CLK | Qnew
0 |  | 0
1 |  | 1
J | K | CLK | Qnew
0 | 0 |  | Qold
0 | 1 |  | 0
1 | 0 |  | 1
1 | 1 |  | Qold
1
1
1
0
0
0
0
1
1
1
0
Outputs change on new clock cycle
T
Q
CLK
J
Q
CLK
K
D
Q
CLK
Q2
Q1
Q0

## Slide 25: Flip-Flops
Example: Assuming the outputs of the following circuit start in a 000 state, determine the outputs for 4 clock cycles
CLK
Cycle | Q2 | Q1 | Q0
start | 0 | 0 | 0
1 | 1 | 1 | 1
T | CLK | Qnew
0 |  | Qold
1 |  | Qold
D | CLK | Qnew
0 |  | 0
1 |  | 1
J | K | CLK | Qnew
0 | 0 |  | Qold
0 | 1 |  | 0
1 | 0 |  | 1
1 | 1 |  | Qold
1
1
1
1
1
1
1
0
0
0
1
Inputs changed due to outputs
T
Q
CLK
J
Q
CLK
K
D
Q
CLK
Q2
Q1
Q0

## Slide 26: Flip-Flops
Example: Assuming the outputs of the following circuit start in a 000 state, determine the outputs for 4 clock cycles
CLK
Cycle | Q2 | Q1 | Q0
start | 0 | 0 | 0
1 | 1 | 1 | 1
2 | 0 | 1 | 0
T | CLK | Qnew
0 |  | Qold
1 |  | Qold
D | CLK | Qnew
0 |  | 0
1 |  | 1
J | K | CLK | Qnew
0 | 0 |  | Qold
0 | 1 |  | 0
1 | 0 |  | 1
1 | 1 |  | Qold
0
1
0
1
1
1
1
0
0
0
1
Outputs change on new clock cycle
T
Q
CLK
J
Q
CLK
K
D
Q
CLK
Q2
Q1
Q0

## Slide 27: Flip-Flops
Example: Assuming the outputs of the following circuit start in a 000 state, determine the outputs for 4 clock cycles
CLK
Cycle | Q2 | Q1 | Q0
start | 0 | 0 | 0
1 | 1 | 1 | 1
2 | 0 | 1 | 0
T | CLK | Qnew
0 |  | Qold
1 |  | Qold
D | CLK | Qnew
0 |  | 0
1 |  | 1
J | K | CLK | Qnew
0 | 0 |  | Qold
0 | 1 |  | 0
1 | 0 |  | 1
1 | 1 |  | Qold
0
1
0
0
0
1
0
1
0
1
0
T
Q
CLK
J
Q
CLK
K
D
Q
CLK
Q2
Q1
Q0
Inputs changed due to outputs

## Slide 28: Flip-Flops
Example: Assuming the outputs of the following circuit start in a 000 state, determine the outputs for 4 clock cycles
CLK
Cycle | Q2 | Q1 | Q0
start | 0 | 0 | 0
1 | 1 | 1 | 1
2 | 0 | 1 | 0
3 | 1 | 0 | 0
T | CLK | Qnew
0 |  | Qold
1 |  | Qold
D | CLK | Qnew
0 |  | 0
1 |  | 1
J | K | CLK | Qnew
0 | 0 |  | Qold
0 | 1 |  | 0
1 | 0 |  | 1
1 | 1 |  | Qold
1
0
0
0
0
1
0
1
0
1
0
T
Q
CLK
J
Q
CLK
K
D
Q
CLK
Q2
Q1
Q0
Outputs change on new clock cycle

## Slide 29: Flip-Flops
Example: Assuming the outputs of the following circuit start in a 000 state, determine the outputs for 4 clock cycles
CLK
Cycle | Q2 | Q1 | Q0
start | 0 | 0 | 0
1 | 1 | 1 | 1
2 | 0 | 1 | 0
3 | 1 | 0 | 0
T | CLK | Qnew
0 |  | Qold
1 |  | Qold
D | CLK | Qnew
0 |  | 0
1 |  | 1
J | K | CLK | Qnew
0 | 0 |  | Qold
0 | 1 |  | 0
1 | 0 |  | 1
1 | 1 |  | Qold
1
0
0
1
0
0
1
1
0
0
0
T
Q
CLK
J
Q
CLK
K
D
Q
CLK
Q2
Q1
Q0
Inputs changed due to outputs

## Slide 30: Flip-Flops
Example: Assuming the outputs of the following circuit start in a 000 state, determine the outputs for 4 clock cycles
CLK
Cycle | Q2 | Q1 | Q0
start | 0 | 0 | 0
1 | 1 | 1 | 1
2 | 0 | 1 | 0
3 | 1 | 0 | 0
4 | 1 | 1 | 0
T | CLK | Qnew
0 |  | Qold
1 |  | Qold
D | CLK | Qnew
0 |  | 0
1 |  | 1
J | K | CLK | Qnew
0 | 0 |  | Qold
0 | 1 |  | 0
1 | 0 |  | 1
1 | 1 |  | Qold
1
1
0
1
0
0
1
1
0
0
0
T
Q
CLK
J
Q
CLK
K
D
Q
CLK
Q2
Q1
Q0
Outputs change on new clock cycle

## Slide 31: Digital Counters
Binary up counter: with N bits, cycles through the numbers from 0 to 2N – 1
  A reset input will force the output to be zero
N-bit
Binary Counter
BN-1
B0
B1
B2
…
CLK
Reset
3-bit up-counter
CLK
B0
B1
B2
0
1
1
0
1
0
0
0
1
0
0
0
1
0
0
1
0
1
1
1
0
1
1
1

## Slide 32: Digital Counters
Ripple counter: with N bits, cycles through the numbers from 0 to 2N – 1
  N JK FFs cascaded together to produce an N-bit up counter
CLK
J
Q
CLK
K
J
Q
CLK
K
J
Q
CLK
K
1
1
1
B0
B1
B2
NB: for 3-bit counter we need 3 FFs
CLK
B0
B1
B2

## Slide 33: Digital Counters
Synchronous counter: with N bits, cycles through the numbers from 0 to 2N – 1
  Input clock drives all FFs simultaneously
T
Q
CLK
T
Q
CLK
T
Q
CLK
CLK
1
B0
B1
B2
CLK
B0
B1
B2

## Slide 34: Registers
Register: an N-bit register is a cascade of N FFs to store data.
  Simplest type is a parallel input, parallel output register
  Read/Write (WR) signal determines if data on the input is written to the FFs
    If WR = 1 data is written
D
Q
CLK
WR
D
Q
CLK
WR
D
Q
CLK
WR
CLK
Read/Write
Q0
Q1
QN-1
D0
D1
D2
Register
N
N
CLK
WR

## Slide 35: Simple Memory
2-to-4
Decoder
a1
a0
00
01
10
11
Register
Register
Register
Register
WR
WR
WR
WR
read/write
d input
q output
This is a functional view.
The key parts are:
address decoder
memory cells (registers)
output selector (mux)
address
Memory
q
n
WR
d
m
m
MEMORY Symbol
n = 2
address
q0
q1
q2
q3
addr