## Slide 1
Date | Day | Class No. | Title | Chapters | HW Due date | Lab Due date | Exam
24 Nov | Mon | 24 | DAC | 15.4 |  |  | 
25 Nov | Tue |  | Recitation |  | HW 10 |  | 
26 Nov | Wed |  | Thanksgiving |  |  |  | 
27 Nov | Thu |  | Thanksgiving |  |  |  | 
28 Nov | Fri |  | Thanksgiving |  |  |  | 
29 Nov | Sat |  |  |  |  |  | 
30 Nov | Sun |  |  |  |  |  | 
1 Dec | Mon |  | Final Review |  |  | LAB 8 | 
2 Dec | Tue |  |  |  |  |  | 
Schedule…

## Slide 2: Conversion
Luke 22:32
32 But I have prayed for thee, that thy faith fail not: and when thou art converted, strengthen thy brethren.

## Slide 3: Lecture 24 – Digital to Analog Converters (DACs)

## Slide 4: ADC/DAC
Power coming from the wall is analog, but most devices (appliances, computers, etc.) are digital thus there must be a conversion
  Analog to digital (ADC) – coming into a device
  Digital to analog (DAC) – going out of a device
Device
ADC
DAC
Digital
Analog
Analog
Actuator
Sensor

## Slide 5: ADC/DAC
ADC
DAC
Digital
Analog
Analog
001110011…
2.23094…
2.23094…
Power coming from the wall is analog, but most devices (appliances, computers, etc.) are digital thus there must be a conversion
  Analog to digital (ADC) – coming into a device
  Digital to analog (DAC) – going out of a device

## Slide 6: Digital to Analog Converter (DAC)
DAC: converts a binary word to an analog output voltage or current
Word length (n): the number of bits in the sequence of 1s and 0s representing an output
  EX:
    0110 – 4-bit word length
    100101 – 6-bit word length
Binary word (B): a sequence of n 1s and 0s
B = bn-1bn-2…b2b1b0
  EX:
    B = 10100101 (n = 8)

## Slide 7: Digital to Analog Converter (DAC)
DAC: converts a binary word to an analog output voltage or current
Resolution δv: minimum step size by which the output voltage (or current) can increment
Output voltage va: the analog value represented by the binary word B
  EX: let n=4
  va = (23·b3 + 22·b2 + 21·b1 + 20·b0)δv
Max output voltage vaMax: the maximum analog value
  EX: let n=4
  vaMax = (23 + 22 + 21 + 20)δv
  = (2n – 1) δv
Example: δv = 1V, B = 10110 (n = 5)
Find vaMax and va
  vaMax = (2n – 1) δv
  = (25 – 1) ∙ 1
  = 31
va = (24·b4 + 23·b3 + 22·b2 + 21·b1 + 20·b0)δv
= (16·1 + 8·0 + 4·1 + 2·1 + 1·0) · 1
= (16 + 4 + 2)
= 22

## Slide 8: Digital to Analog Converter (DAC)
Building a DAC:
use a summing amplifier
–
+
+
vo
–
+
–
+
–
+
–
RSn
RS2
RS1
vSn
vS2
vS1
RF
–
+
+
va
–
R1
Rn-2
Rn-1
RF
R0
vin
bn-1
bn-2
b1
b0
Summing amplifier
DAC

## Slide 9: Digital to Analog Converter (DAC)
Building a DAC:
the analog output (va) is proportional to the binary word B
–
+
+
va
–
R1
Rn-2
Rn-1
RF
R0
vin
bn-1
bn-2
b1
b0
Choose
THUS
vsi in summing amplifier

## Slide 10: Digital to Analog Converter (DAC)
Example1: vin = 5V, B = 1011, R0 = 32kΩ, RF = 64kΩ
Find Rn and va
–
+
+
va
–
R1
Rn-2
Rn-1
RF
R0
vin
bn-1
bn-2
b1
b0

## Slide 11: Digital to Analog Converter (DAC)
Example1: vin = 5V, B = 1011, R0 = 32kΩ, RF = 64kΩ
Find Rn and va
–
+
+
va
–
R1
R2
R3
RF
R0
5 V
b3 = 1
b2 = 0
b1 = 1
b0 = 1

## Slide 12: Digital to Analog Converter (DAC)
Building a DAC:
  the analog output (va) has a step-like appearance because of the discrete nature of a binary signal
  The resolution (coarseness of the “staircase”) can be adjusted by changing the word length (the number of bits)
Approximated using 2-bits
Approximated using 3-bits
δv
δv

## Slide 13: Digital to Analog Converter (DAC)
Example2: find the smallest resolution δv of an 8-bit DAC
vaMax = 12V
–
+
+
va
–
R1
Rn-2
Rn-1
RF
R0
vin
bn-1
bn-2
b1
b0

## Slide 14: Digital to Analog Converter (DAC)
Example2: find the smallest resolution δv of an 8-bit DAC
vaMax = 12V
–
+
+
va
–
R1
Rn-2
Rn-1
RF
R0
vin
bn-1
bn-2
b1
b0

## Slide 15: Digital to Analog Converter (DAC)
Example3: find an expression for the number of bits required in a DAC for a given range and resolution
range = vaMax – vaMin
resolution = δv
–
+
+
va
–
R1
Rn-2
Rn-1
RF
R0
vin
bn-1
bn-2
b1
b0

## Slide 16: Digital to Analog Converter (DAC)
Example3: find an expression for the number of bits required in a DAC for a given range and resolution
range = vaMax – vaMin
resolution = δv
–
+
+
va
–
R1
Rn-2
Rn-1
RF
R0
vin
bn-1
bn-2
b1
b0

## Slide 17: Digital to Analog Converter (DAC)
Example4: find the number of bits required in a DAC given that:
range = 10V
resolution = 10 mV
–
+
+
va
–
R1
Rn-2
Rn-1
RF
R0
vin
bn-1
bn-2
b1
b0

## Slide 18: Digital to Analog Converter (DAC)
Example4: find the number of bits required in a DAC given that:
range = 10V
resolution = 10 mV
–
+
+
va
–
R1
Rn-2
Rn-1
RF
R0
vin
bn-1
bn-2
b1
b0

## Slide 19: Digital to Analog Converter (DAC)
Example5: find the resistor values for a DAC with:
range = 15V
δv = 1V
vin = 5V
RF = 2kΩ
–
+
+
va
–
R1
Rn-2
Rn-1
RF
R0
vin
bn-1
bn-2
b1
b0

## Slide 20: Digital to Analog Converter (DAC)
Example5: find the resistor values for a DAC with:
range = 15V
δv = 1V
vin = 5V
RF = 2kΩ
–
+
+
va
–
R1
Rn-2
Rn-1
RF
R0
vin
bn-1
bn-2
b1
b0

## Slide 21: Digital to Analog Converter (DAC)
Example5: find the resistor values for a DAC with:
range = 15V
δv = 1V
vin = 5V
RF = 2kΩ
–
+
+
va
–
R1
Rn-2
Rn-1
RF
R0
vin
bn-1
bn-2
b1
b0

## Slide 22: Digital to Analog Converter (DAC)
Example5: find the resistor values for a DAC with:
range = 15V
δv = 1V
vin = 5V
RF = 2kΩ
–
+
+
va
–
R1
Rn-2
Rn-1
RF
R0
vin
bn-1
bn-2
b1
b0