## Slide 1
Date | Day | Class No. | Title | Chapters | HW Due date | Lab Due date | Exam
10 Sept | Wed | 3 | Power | 2.4 – 2.5 |  |  | 
11 Sept | Thu |  |  |  |  |  | 
12 Sept | Fri |  | Recitation |  | HW1 |  | 
13 Sept | Sat |  |  |  |  |  | 
14 Sept | Sun |  |  |  |  |  | 
15 Sept | Mon | 4 | Ohm’s Law | 2.5 – 2.6 |  | LAB 1 | 
16 Sept | Tue |  |  |  |  |  | 
17 Sept | Wed | 5 | Ohm’s Law | 2.6 |  |  | 
Schedule…

## Slide 2: True Power – The Book of Mormon
Alma 37:14, 16, 18
14 And now remember, my son, that God has entrusted you with these things, which are sacred, which he has kept sacred, and also which he will keep and preserve for a wise purpose in him, that he may show forth his power unto future generations.
16 But if ye keep the commandments of God, and do with these things which are sacred according to that which the Lord doth command you, (for you must appeal unto the Lord for all things whatsoever ye must do with them) behold, no power of earth or hell can take them from you, for God is powerful to the fulfilling of all his words.
18 For he promised unto them that he would preserve these things for a wise purpose in him, that he might show forth his power unto future generations.
Mormon 8:15, 16, 22, 26, 28
15 For none can have power to bring it to light save it be given him of God; for God wills that it shall be done with an eye single to his glory, or the welfare of the ancient and long dispersed covenant people of the Lord.
16 And blessed be he that shall bring this thing to light; for it shall be brought out of darkness unto light, according to the word of God; yea, it shall be brought out of the earth, and it shall shine forth out of darkness, and come unto the knowledge of the people; and it shall be done by the power of God.
22 For the eternal purposes of the Lord shall roll on, until all his promises shall be fulfilled.
26 And no one need say they shall not come, for they surely shall, for the Lord hath spoken it; for out of the earth shall they come, by the hand of the Lord, and none can stay it; and it shall come in a day when it shall be said that miracles are done away; and it shall come even as if one should speak from the dead.
28 Yea, it shall come in a day when the power of God shall be denied…

## Slide 3: Lecture 3 – Electric Power

## Slide 4: Energy vs. Power
Consider filling a pool of water
  The rate (power) at which the water comes out determines how long it will take to fill the pool
  The water that has filled the pool represents energy
  Both pools have the same amount of water (energy) – the rate at which they were filled (power) was different
20 minutes
10 minutes

## Slide 5: Energy vs. Power
Power: the rate at which energy (electricity) is consumed
  How fast energy can be generated/delivered to/from an electrical device
Energy: the ability to do work
  EX: a battery, a capacitor, a fuel cell
joule (J): electric energy unit.
1 J = the work required to move an electrical charge of 1C through 1V
1 J = the energy required to lift a small apple (102 g) one meter against Earth's gravity.
1 J = the energy required to heat one gram of dry, cool air by 1 degree Celsius.
1 J = 6.241506363091018 eV (electron-volts)
1 J = 2.7778 x10-7 kilowatt-hour
kilowatt-hour (kWh): electric energy unit.

## Slide 6: Electric Power
Electric Power: the power generated by an active element, or dissipated by a passive element is equal to the product of: voltage across the element and current flowing through it
Watt (W): electric power unit.
1 Watt = 1 joule/second (J/s)
1 Watt = 1 volt-amp (VA)

## Slide 7: Electric Power
Passive sign convention: power dissipated by a load is a positive quantity – the power generated by a source is positive
+
vab
_
a
b
i
vba
_
a
b
i
+
Active Element (source)
power dissipated = -vi
power generated = vi
Passive Element (load)
power dissipated = vi
power generated = -vi
Positive voltage
Negative voltage

## Slide 8: Passive Sign Convention
Choose an arbitrary direction for current flow
Label polarities of all active elements (sources) based on direction of current flow
Label polarities of all passive elements (loads) based on direction of current flow
Compute the power dissipated by each element based on:
  If current flows into the positive terminal of the element, the power dissipated is positive (power is absorbed)
  If current flows into the negative terminal of the element the power dissipated is negative (power is delivered)

## Slide 9: Electric Power
Example1: find the power dissipated by each element.
  va = 8V, vb = 4V, i = 0.1A
Load A
Load B
Vs

## Slide 10: Electric Power
Example1: find the power dissipated by each element.
  va = 8V, vb = 4V, i = 0.1A
Assume a clockwise direction of current flow
Load A
Load B
Vs
i

## Slide 11: Electric Power
Example1: find the power dissipated by each element.
  va = 8V, vb = 4V, i = 0.1A
Assume a clockwise direction of current flow
Label polarity of sources according to current flow
Load A
Load B
+
_
Vs
i

## Slide 12: Electric Power
Example1: find the power dissipated by each element.
  va = 8V, vb = 4V, i = 0.1A
Assume a clockwise direction of current flow
Label polarity of sources according to current flow
Label polarity of loads according to current flow
+ va –
+
vb
–
Load A
Load B
+
_
Vs
i

## Slide 13: Electric Power
Example1: find the power dissipated by each element.
  va = 8V, vb = 4V, i = 0.1A
Assume a clockwise direction of current flow
Label polarity of sources according to current flow
Label polarity of loads according to current flow
Calculate power dissipated in each element
+ va –
+
vb
–
Load A
Load B
+
_
Vs
i

## Slide 14: Electric Power
Example1: find the power dissipated by each element.
  va = 8V, vb = 4V, i = 0.1A
Assume a clockwise direction of current flow
Label polarity of sources according to current flow
Label polarity of loads according to current flow
Calculate power dissipated in each element
+ va –
+
vb
–
Load A
Load B
+
_
Vs
i

## Slide 15: Electric Power
Example1: find the power dissipated by each element.
  va = 8V, vb = 4V, i = 0.1A
Assume a clockwise direction of current flow
Label polarity of sources according to current flow
Label polarity of loads according to current flow
Calculate power dissipated in each element
+ va –
+
vb
–
Load A
Load B
+
_
Vs
i

## Slide 16: Electric Power
Example1: find the power dissipated by each element.
  va = 8V, vb = 4V, i = 0.1A
Assume a counter-clockwise direction of current flow
Label polarity of sources according to current flow
Label polarity of loads according to current flow
Calculate power dissipated in each element
– va +
–
vb
+
Load A
Load B
–
+
Vs
i

## Slide 17: Electric Power
Example1: find the power dissipated by each element.
  va = 8V, vb = 4V, i = 0.1A
– va +
–
vb
+
Load A
Load B
–
+
Vs
i
NB: Power is conserved (power supplied always equals power consumed):
Ps + Pa + Pb = 0

## Slide 18: Electric Power
Example2: find the power dissipated by each element.
B
E
+
10V
–
– 3V +
A
D
C
– 5V +
ie = 2A
id =3A

## Slide 19: Electric Power
Example2: find the power dissipated by each element.
B
E
+
10V
–
– 3V +
A
D
C
– 5V +
ie = 2A
id =3A
a
ia

## Slide 20: Electric Power
Example2: find the power dissipated by each element.
B
E
+
10V
–
– 3V +
A
D
C
– 5V +
ie = 2A
id =3A
ia = 5A
Loop1
+
va
–

## Slide 21: Electric Power
Example2: find the power dissipated by each element.
B
E
+
10V
–
– 3V +
A
D
C
– 5V +
ie = 2A
id =3A
ia = 5A
Loop2
+
12V
–
+
vd
–
NB: since load D and load E share the same node their voltages will be the same

## Slide 22: Electric Power
Example2: find the power dissipated by each element.
B
E
+
10V
–
– 3V +
A
D
C
– 5V +
ie = 2A
id =3A
ia = 5A
+
12V
–
+
10V
–

## Slide 23: Electric Power
Example3: The battery supplies a total of 10mW. What is i3?
  i1 = 1mA, i2 = 1.5mA
i
i
i1
i2
i3
4V
+
_

## Slide 24: Electric Power
Example3: The battery supplies a total of 10mW. What is i3?
  i1 = 1mA, i2 = 1.5mA
i
i
i1
i2
i3
4V
+
_
+
_
+
_
+
_

## Slide 25: i–v Element Characteristics
The relationship between current (i) and voltage (v) at the terminals of a circuit element defines the behaviour of that element within the circuit
+
_
i
v
If a voltage is imposed across the terminals of the element the voltage itself (v) and the current that will flow (i) form a unique pair of values.
  measuring the current while the voltage varies is known as the i–v characteristic
  with the i–v characteristic voltage (current) can be determined from a given current (voltage)
  power can also be determined

## Slide 26: i–v Element Characteristics
i–v characteristic can be given as:
  a function
  a graph

## Slide 27: i–v Element Characteristics
Power generated vs. power dissipated quadrants
Generated
(sources)
Generated
(sources)
Dissipated
(loads)
Dissipated
(loads)

## Slide 28: i–v Element Characteristics
Elements that source and dissipate power
  Photovoltaic – solar cells, photodiodes, photodetectors
Dissipate
Dissipate
Generate

## Slide 29: i–v Element Characteristics
Ideal DC current source
  3A source
Ideal DC voltage source
  6V source
+
_
Vs
Is