## Slide 1
Date | Day | Class No. | Title | Chapters | HW Due date | Lab Due date | Exam
15 Sept | Mon | 4 | Ohm’s Law | 2.5 – 2.6 |  | LAB 1 | 
16 Sept | Tue |  |  |  |  |  | 
17 Sept | Wed | 5 | Ohm’s Law | 2.6 |  |  | 
18 Sept | Thu |  |  |  |  | LAB 1 | 
29 Sept | Fri |  | Recitation |  | HW 2 |  | 
20 Sept | Sat |  |  |  |  |  | 
21 Sept | Sun |  |  |  |  |  | 
22 Sept | Mon | 6 | Practical Sources | 2.6 – 2.8 |  | LAB 2 | 
23 Sept | Tue |  |  |  |  |  | 
Schedule…

## Slide 2: High Resistance to Evil, Low Resistance to Good
James 4:7
7 Submit yourselves therefore to God. Resist the devil, and he will flee from you.
Alma 61:14
14 Therefore, my beloved brother, Moroni, let us resist evil, and whatsoever evil we cannot resist with our words, yea, such as rebellions and dissensions, let us resist them with our swords, that we may retain our freedom, that we may rejoice in the great privilege of our church, and in the cause of our Redeemer and our God.

## Slide 3: Lecture 4 – Resistance & Ohm’s Law

## Slide 4: Resistance
Resistance (R): opposition to the flow of current
  Magnitude depends on electrical properties of the material
  All circuit elements exhibit some resistance
  May be undesirable
  Causes electric energy to be transformed into heat
  Element symbols:
Ohm (Ω): electric resistance unit.
1 Ohm = 1 Volt/Ampere (V/A)

## Slide 5: Conductance
Conductance (G): the inverse of resistance
siemens (S): electric conductance unit.
1 siemens = 1 Ampere/Volt (A/V)

## Slide 6: Resistance
Resistivity (ρ): a materials property which determines resistance
Conductivity (σ): the inverse of resistivity (determines conductance)
l
A
+
v
_
R
i

## Slide 7: Resistance
Common resistors are made of cylindrical sections of carbon (resistivity ρ = 3.5x10-5Ω-m)
b4
b3
b2
b1
black | 0 | Blue | 6
brown | 1 (1%) | violet | 7
red | 2 (2%) | gray | 8
orange | 3 | white | 9
yellow | 4 | silver | -2 (10%)
green | 5 | gold | -1 (5%)
 |  | None | (20%)

## Slide 8: Resistance
Code | Ω | Mult | Ω | Mult | k Ω | Mult | k Ω | Mult | k Ω | Mult
Brn-blk | 10 | Black | 100 | Brown | 1.0 | Red | 10 | Orange | 100 | Yellow
Brn-red | 12 | Black | 120 | Brown | 1.2 | Red | 12 | Orange | 120 | Yellow
Brn-grn | 15 | Black | 150 | Brown | 1.5 | Red | 15 | Orange | 150 | Yellow
Brn-gry | 18 | Black | 180 | Brown | 1.8 | Red | 18 | Orange | 180 | Yellow
Red-red | 22 | Black | 220 | Brown | 2.2 | Red | 22 | Orange | 220 | Yellow
Red-vlt | 27 | Black | 270 | Brown | 2.7 | Red | 27 | Orange | 270 | Yellow
Org-org | 33 | Black | 330 | Brown | 3.3 | Red | 33 | Orange | 330 | Yellow
Org-wht | 39 | Black | 390 | Brown | 3.9 | Red | 39 | Orange | 390 | Yellow
Ylw-vlt | 47 | Black | 470 | Brown | 4.7 | Red | 4.7 | Orange | 470 | Yellow
Grn-blu | 56 | Black | 560 | Brown | 5.6 | Red | 5.6 | Orange | 560 | Yellow
Blu-gry | 68 | Black | 680 | Brown | 6.8 | Red | 6.8 | Orange | 680 | Yellow
Gry-red | 82 | Black | 820 | Brown | 8.2 | Red | 8.2 | Orange | 820 | Yellow

## Slide 9: Resistance
Example1: what is the value of the resistor?
b4
b3
b2
b1
black | 0 | Blue | 6
brown | 1 (1%) | violet | 7
red | 2 (2%) | gray | 8
orange | 3 | white | 9
yellow | 4 | silver | -2 (10%)
green | 5 | gold | -1 (5%)
 |  | None | (20%)

## Slide 10: Resistance
Example1: what is the value of the resistor?
b4
b3
b2
b1
black | 0 | Blue | 6
brown | 1 (1%) | violet | 7
red | 2 (2%) | gray | 8
orange | 3 | white | 9
yellow | 4 | silver | -2 (10%)
green | 5 | gold | -1 (5%)
 |  | None | (20%)

## Slide 11: Resistance
Example2: what resistor has a value of 6.2M Ω?
b4
b3
b2
b1
black | 0 | Blue | 6
brown | 1 (1%) | violet | 7
red | 2 (2%) | gray | 8
orange | 3 | white | 9
yellow | 4 | silver | -2 (10%)
green | 5 | gold | -1 (5%)
 |  | None | (20%)

## Slide 12: Resistance
Example2: what resistor has a value of 6.2M Ω?
b4
b3
b2
b1
Blue
Red
Green
black | 0 | Blue | 6
brown | 1 (1%) | violet | 7
red | 2 (2%) | gray | 8
orange | 3 | white | 9
yellow | 4 | silver | -2 (10%)
green | 5 | gold | -1 (5%)
 |  | None | (20%)

## Slide 13: Ohm’s Law
The voltage across an element is directly proportional to the current flow through it
OR
+
v
_
R
i
1/R

## Slide 14: Ohm’s Law
Ohm’s law is only a simplification
  Ohm’s law is not applicable:
    At high voltages or currents
    At high frequencies
    Over long distances
    For some materials
For our class Ohm’s law will apply!

## Slide 15: Ohm’s Law
Ohm’s Law only applies to a portion of an electrical element’s the i–v graph

## Slide 16: Ohm’s Law
Example3: What is the resistance of the element with the following i–v characteristic?

## Slide 17: Ohm’s Law
Example3: What is the resistance of the element with the following i–v characteristic?
1/R

## Slide 18: Power Rating
power rating: maximum allowable power dissipation
  Common power rating is ¼ W
Exceeding the power rating for an electrical element will cause the element to burn up!
  Always consider power ratings!!

## Slide 19: Power Rating
Example4: With a ¼ W rating, what is the minimum resistor size (R) that can be used in the following:
Vs
+
_
i
+
R1
–
1.5V
Vs1
+
_
i
+
R2
–
1.5V
Vs2
– +
1.5V

## Slide 20: Power Rating
Example4: With a ¼ W rating, what is the minimum resistor size (R) that can be used in the following:
Vs
+
_
i
+
R1
–
1.5V
Vs1
+
_
i
+
R2
–
1.5V
Vs2
– +
1.5V

## Slide 21: Power Rating
Example4: With a ¼ W rating, what is the minimum resistor size (R) that can be used in the following:
Vs
+
_
i
+
R1
–
1.5V
Vs1
+
_
i
+
R2
–
1.5V
Vs2
– +
1.5V
NB: Doubling the amount of voltage has a quadratic effect on minimum resistor size

## Slide 22: Power Rating
Example5: find the power supplied by the battery
  Vs = 3V, i1 = 0.2mA, i2 = 0.4mA, i3 = 1.2mA
is
i1
i2
i3
+
R1
–
Vs
+
_
+
R2
–
+
R3
–

## Slide 23: Power Rating
Example5: find the power supplied by the battery
  Vs = 3V, i1 = 0.2mA, i2 = 0.4mA, i3 = 1.2mA
is
i1
i2
i3
+
R1
–
Vs
+
_
+
R2
–
+
R3
–
Node a

## Slide 24: Power Rating
is
i1
i2
i3
+
R1
–
Vs
+
_
+
R2
–
+
R3
–
Example6: find the voltages and resistances of R1, R2, R3
  Vs = 3V, i1 = 0.2mA, i2 = 0.4mA, i3 = 1.2mA

## Slide 25: Power Rating
Example6: find the voltages and resistances of R1, R2, R3
  Vs = 3V, i1 = 0.2mA, i2 = 0.4mA, i3 = 1.2mA
is
i1
i2
i3
+
R1
–
Vs
+
_
+
R2
–
+
R3
–

## Slide 26: Power Rating
is
i1
i2
i3
+
R1
–
Vs
+
_
+
R2
–
+
R3
–
Example6: find the voltages and resistances of R1, R2, R3
  Vs = 3V, i1 = 0.2mA, i2 = 0.4mA, i3 = 1.2mA