## Slide 1
Date | Day | Class No. | Title | Chapters | HW Due date | Lab Due date | Exam
17 Sept | Wed | 5 | Ohm’s Law | 2.6 |  |  | 
18 Sept | Thu |  |  |  |  | LAB 1 | 
19 Sept | Fri |  | Recitation |  | HW 2 |  | 
20 Sept | Sat |  |  |  |  |  | 
21 Sept | Sun |  |  |  |  |  | 
22 Sept | Mon | 6 | Things Practical | 2.6 – 2.8 |  | LAB 2 | 
23 Sept | Tue |  |  |  |  |  | 
24 Sept | Wed | 7 | Network Analysis | 3.1 – 3.2 |  |  | 
Schedule…

## Slide 2: Divided We Fall
Matthew 12:25-26
25 And Jesus knew their thoughts, and said unto them, Every kingdom divided against itself is brought to desolation; and every city or house divided against itself shall not stand:
Nephi 7:2
2 And the people were divided one against another; and they did separate one from another into tribes, every man according to his family and his kindred and friends; and thus they did destroy the government of the land.

## Slide 3: Lecture 5 – Resistance & Ohm’s Law

## Slide 4: Open and Short Circuits
Short circuit: a circuit element across which the voltage is zero regardless of the current flowing through it
  Resistance approaches zero
  Flow of current is unimpeded
  ex: an ideal wire
    In reality there is a small resistance
i
R = 0
v = 0
v
+
–

## Slide 5: Open and Short Circuits
Undesirable short circuit – accidental connection between two nodes that are meant to be at different voltages. The resulting excessive current causes: overheating, fire, or explosion

## Slide 6: Open and Short Circuits
Open circuit: a circuit element through which zero current flows regardless of the voltage applied to it
  Resistance approaches infinity
  No current flows
  ex: a break in a circuit
    At sufficiently high voltages arcing occurs
i
R ∞
i = 0
v
+
–

## Slide 7: Open and Short Circuits
i2
+
v2
–
vs
+
_
+
v3
–
+ v1 –
R2
R1
R3
i3
i1
Example: What happens to R2 and R3 if R1 is shorted?
    Vs = 2V, R1 = 2Ω, R2 = R3 = 4Ω, i1 = 500mA
    R2 and R3 = ¼ W rating, R1 = ½ W rating

## Slide 8: Open and Short Circuits
Example: What happens to R2 and R3 if R1 is shorted?
    Vs = 2V, R1 = 2Ω, R2 = R3 = 4Ω, i1 = 500mA
    R2 and R3 = ¼ W rating, R1 = ½ W rating
i2
+
v2
–
vs
+
_
+
v3
–
+ v1 –
R2
R1
R3
i3
i1

## Slide 9: Open and Short Circuits
i2
+
v2
–
vs
+
_
+
v3
–
+ v1 –
R2
R1
R3
i3
i1
Example: What happens to R2 and R3 if R1 is shorted?
    Vs = 2V, R1 = 2Ω, R2 = R3 = 4Ω, i1 = 500mA
    R2 and R3 = ¼ W rating, R1 = ½ W rating

## Slide 10: Open and Short Circuits
i2
+
v2
–
vs
+
_
+
v3
–
R2
R3
i3
i1
Example: What happens to R2 and R3 if R1 is shorted?
    Vs = 2V, R1 = 2Ω, R2 = R3 = 4Ω, i1 = 500mA
    R2 and R3 = ¼ W rating, R1 = ½ W rating
BAD! R2 and R3 are damaged

## Slide 11: Series Resistors
Series Rule: two or more circuit elements are said to be in series if the current from one element exclusively flows into the next element.
  From KCL: all series elements have the same current
R1
∙ ∙ ∙
∙ ∙ ∙
R2
R3
Rn
RN
REQ

## Slide 12: Series Resistors
Demonstration of series rule: apply KVL and Ohm’s law on the circuit
Vs
+
_
+ v1 –
R1
– v3 +
R3
R2
+
v2
–
1.5V
i

## Slide 13: Series Resistors
Voltage divider: the voltage across each resistor in a series circuit is directly proportional to the ratio of its resistance to the total series resistance of the circuit
NB: the ratio will always be <= 1

## Slide 14: Series Resistors
Voltage divider: the voltage across each resistor in a series circuit is directly proportional to the ratio of its resistance to the total series resistance of the circuit
Vs
+
_
+ v1 –
R1
– v3 +
R3
R2
+
v2
–
1.5V
i

## Slide 15: Series Resistors
Example1: Determine v3
  Vs = 3V, R1 = 10Ω, R2 = 6Ω, R3 = 8Ω
Vs
+
_
– v1 +
R1
+ v3 –
R3
R2
+
v2
–
i

## Slide 16: Series Resistors
Example1: Determine v3
  Vs = 3V, R1 = 10Ω, R2 = 6Ω, R3 = 8Ω
Vs
+
_
– v1 +
R1
+ v3 –
R3
R2
+
v2
–
i

## Slide 17: Parallel Resistors
Parallel Rule: two or more circuit elements are said to be in parallel if the elements share the same terminals
  From KVL: the elements will have the same voltage
+
R1
–
+
R2
–
+
R3
–
+
Rn
–
+
RN
–
+
REQ
–
NB: the parallel combination of two resistors is often written: R1 || R2

## Slide 18: Parallel Resistors
Demonstration of parallel rule: apply KCL and Ohm’s law on the circuit
i1
i2
i3
+
R1
–
is
+
R2
–
+
R3
–
+
v
–
Node a

## Slide 19: Parallel Resistors
Current divider: the current in a parallel circuit divides in proportion to the resistances of the individual parallel elements
NB: the ratio will always be <= 1

## Slide 20: Parallel Resistors
Current divider: the current in a parallel circuit divides in proportion to the resistances of the individual parallel elements
i1
i2
i3
+
R1
–
is
+
R2
–
+
R3
–
NB: it makes sense that the smaller the resistor, the larger the amount of current that will flow.

## Slide 21: Parallel Resistors
Example2: find i1
  R1 = 10Ω, R2 = 2 Ω, R3 = 20 Ω, Is = 4A
i1
i2
i3
–
R1
+
is
–
R2
+
–
R3
+

## Slide 22: Parallel Resistors
Example2: find i1
  R1 = 10Ω, R2 = 2 Ω, R3 = 20 Ω, Is = 4A
i1
i2
i3
–
R1
+
is
–
R2
+
–
R3
+

## Slide 23: Parallel Resistors
Example2: find i1
  R1 = 10Ω, R2 = 2 Ω, R3 = 20 Ω, Is = 4A
i1
i2
i3
–
R1
+
is
–
R2
+
–
R3
+

## Slide 24: Parallel Resistors
The parallel combination of resistors is often written:
  For two resistors: R1 || R2
  For three resistors: R1 || R2 || R3
  etc.
In each case REQ for the parallel combination must be found
+
R1
–
+
R2
–
+
R3
–
+
R1
–
+
R2
–
+
R1|| R2|| R3
–
+
R1|| R2
–

## Slide 25: Parallel Resistors
Example3: find v
  vs = 5V, R1 = 1kΩ, R2 = 1kΩ
is
+
R2
–
vs
+
_
+
R3
–
+ R1 –
+
v
–

## Slide 26: Parallel Resistors
Example3: find v
  vs = 5V, R1 = 1kΩ, R2 = 1kΩ
is
+
R2
–
vs
+
_
+
R3
–
+ R1 –
+
v
–
is
R2 || R3
vs
+
_
+ R1 –
+
v
–

## Slide 27: Parallel Resistors
Example3: find v
  vs = 5V, R1 = 1kΩ, R2 = 1kΩ
is
R2 || R3
vs
+
_
+ R1 –
+
v
–

## Slide 28: Parallel Resistors
Example3: find v
  vs = 5V, R1 = 1kΩ, R2 = 1kΩ
is
R2 || R3
vs
+
_
+ R1 –
+
v
–
NB: notice how R3 controls v

## Slide 29: Parallel Resistors
Example3: find v
  vs = 5V, R1 = 1kΩ, R2 = 1kΩ
is
R2 || R3
vs
+
_
+ R1 –
+
v
–
NB: notice how R3 controls v

## Slide 30: Parallel Resistors
Example3: find v
  vs = 5V, R1 = 1kΩ, R2 = 1kΩ
NB: notice how R3 controls v
is
+
R2
–
vs
+
_
+
R3
–
+ R1 –
+
v
–

## Slide 31: Parallel Resistors
Example3: find v
  vs = 5V, R1 = 1kΩ, R2 = 1kΩ
is
+
R2
–
vs
+
_
+ R1 –
+
v
–

## Slide 32: Parallel Resistors
Example3: find v
  vs = 5V, R1 = 1kΩ, R2 = 1kΩ
is
+
R2
–
vs
+
_
+ R1 –
+
v
–