## Slide 1: Temperature of a 100 W Light Bulb Filament
Joran Booth and Peter Hyatt
ME 340
Winter 2009

## Slide 2: Heat Transfer Problem
Measured the electrical power dissipated
Measured the bulb surface temperature and the ambient temperature
Measured the diameter of the light bulb
Measured the thickness of the glass
Assumptions:
Near vacuum inside the light bulb
Geometry is a sphere
The radiation is a point source
Filament treated as a sphere
All electrical work converted to heat

## Slide 3: Solution
Online sources show: T = 2550ºC
Ts = 95ºC
Tfilament= ?
knitrogen
= 81 W/m·K
As, ε
qin = 96 W
60 mm Ø
0.5 mm thick
Glass
Vacuum
Tavg | ρ | cP | μ | ν | k | α | Pr | beta
332 | 1.0549 | 1008 | 2.00E-05 | 1.91E-05 | 2.87E-02 | 2.72E-05 | 0.703 | 3.01E-03
Øfil = | 0.06149 | σ = | 5.67E-08 | hr1 = | 481.0875139 | R1 = | -0.0434 | 
Øinner = | 0.0595 | Tin = | 368 | hr2 = | 8.111165792 | R2 = | 7.00E-01 | 
Øouter = | 0.06 | TS = | 368 | h = | 6.56E+00 | R3 = | 0.00028 | 
kN = | 2 | T∞ = | 300 | Nu = | 13.71767276 | R4 = | 53.901 | 
kglass = | 81 | q = | 96 W | Ra = | 8.34E+05 | R5 = | 43.6038 | 
Afil = | 0.00283 | εglass = | 0.95 |  |  | Rtotal = | 24.8045 | without R1
Aglass = | 2.97E-03 | εW = | 0.38 |  |  | Tfilament = | 2681 | K
 |  | Ts = | 2681 |  |  |  |  | 

## Slide 4: Results
Chart: 
| 0.38 | 0.27 | 0.18
Emissivity vs. Temperature | 4316.408 | 5009.9645 | 4983.3733
Chart: Area vs. Temperature
| 2.97E-3 | 2.97E-5 | 2.9700000000000003E-7
Area versus Temperature | 2681.2298 | 4316.408 | 11709.2714

## Slide 5: Conclusions and Recommendations
The temperature is between 4500 to 2500˚C.
Main contributors to Tfilament:
  Surface Area of Filament
  Vacuum v. Conduction thru gas
Measure different filament styles
Verify/modify assumptions with other measurements

## Slide 6: Appendix
http://answers.yahoo.com/question/index?qid=20080508134327AAlv437 .
Fundamentals of Heat and Mass Transfer, Incropera, 6th Edition.
http://members.misty.com/don/bulb1.html

## Slide 7: Additional Graphs
Chart: 
| 2.97E-3 | 2.97E-5 | 2.7000000000000001E-7
Area vs. Temperature | 2615.4411 | 2642.9403 | 2933.91
Chart: 
| 0.38 | 0.27 | 0.18
Emissivity vs. Temperature | 2642.9403 | 2642.9714 | 2644.4934
Both graphs based on assumption of pure nitrogen inside bulb with no convection

## Slide 8: Calcuations
A1 = | 2.97E-03 | ε1 = | 0.38 | Ts = | 2681 | K | A1 = | 2.97E-05 | ε1 = | 0.38 | Ts = | 4316 | K | A1 = | 2.97E-07 | ε1 = | 0.38 | Ts = | 11709 | K
 |  | Ts = | 2681 |  |  |  |  |  | Ts = | 4320 |  |  |  |  |  | Ts = | 11690 |  |  | 
A1 = | 2.97E-05 | ε1 = | 0.38 | Ts = | 4316 | K | A1 = | 2.97E-05 | ε1 = | 0.27 | Ts = | 5010 | K | A1 = | 2.97E-05 | ε1 = | 0.18 | Ts = | 4983 | K
 |  | Ts = | 4320 |  |  |  |  |  | Ts = | 4320 |  |  |  |  |  | Ts = | 4984 |  |  | 
A1 = | 2.97E-03 | ε1 = | 0.38 | Ts = | 2615 | K | A1 = | 2.97E-05 | ε1 = | 0.38 | Ts = | 2643 | K | A1 = | 2.70E-07 | ε1 = | 0.38 | Ts = | 2934 | K
 |  | Ts = | 2615 |  |  |  |  |  | Ts = | 2643 |  |  |  |  |  | Ts = | 2933.96 |  |  | 
A1 = | 2.97E-05 | ε1 = | 0.38 | Ts = | 2643 | K | A1 = | 2.97E-05 | ε1 = | 0.27 | Ts = | 2643 | K | A1 = | 2.70E-05 | ε1 = | 0.18 | Ts = | 2644 | K
 |  | Ts = | 2643 |  |  |  |  |  | Ts = | 2643 |  |  |  |  |  | Ts = | 2644 |  |  | 
Assuming a vacuum
Assuming nitrogen filled