## Slide 1: Sensor Pipe Heat Transfer By: Brandon Woodland & William Gough
Purpose
To determine the temperature gradient on a closed pipe extension from an exhaust pipe

## Slide 2: Modeling Process
Assumptions
  Quiescent air around pipes
  No convection interaction at pipe junction
  Assumed to simplify calculation of radiant heat transfer
  No air flow or turbulence in sensor pipe
  Assumed so surface of pipe can be approximated as a flat surface
  Sensor pipe treated as fin coming off of main pipe
Ls
y
x
TLs (Target Temperature)
TLe
T0
Tmie
TmLe
This schematic drawing of the experiment helps explain the development of modeling equations and the meanings of nomenclature defined in the Excel sheet.
Exhaust Pipe (open end)
Sensor Pipe (closed end)
Hot Air In

## Slide 3: Modeling Equations
Convection Coefficients
Mean air flow temperature of exhaust pipe
Sensor Pipe Base Temperature
Temperature of Sensor pipe at length

## Slide 4
Thermocouple
Sensor Pipe
Exhaust Pipe
Heat Gun
Test Setup

## Slide 5
Summary |  |  | 
Test 1 | Measured | Predicted | % Error
TmLe [C] | 100.78 | 105.65 | 4.62%
TLe [C] | 41.97 | 97.09 | 56.77%
TLs [C] | 27.70 | 28.92 | 4.22%
Test 2 |  |  | 
TmLe [C] | 100.57 | 98.04 | -2.57%
TLe [C] | 65.77 | 88.34 | 25.55%
TLs [C] | 21.33 | 23.45 | 9.01%
Measured vs. calculated values with percent error. Note the good accuracy of the final calculation (TLs) despite considerable error in intermediate calculation (TLe).
Constants |  |  | Exhaust Pipe Properties |  |  | Exhaust Pipe Inside Air |  |  | Sensor Pipe Properties |  |  |  |  | 
Tinf [K] | 292.00 |  | T0 | 342.47 |  | TmLe_guess [K] | 373.57 |  | TLs_guess [K] | 294.33 |  |  |  | 
g [m/s^2] | 9.82 |  | Dei [in] | 1.631 |  | Tbar_e [K] | 373.22 |  | Dsi [in] | 0.62 |  |  |  | 
 |  |  | Deo [in] | 1.75 |  | nu_ei [m^2/s] | 2.35E-05 |  | Dso [in] | 0.72 |  |  |  | 
Input Data |  |  | Le [in] | 11.8125 |  | cp_ei [J/(kg-K)] | 1011 |  | Ls [in] | 7.375 |  |  |  | 
Tinf [C] | 19.00 |  | Dei [m] | 0.0414 |  | k_ei [W/(m-K)] | 3.18E-02 |  | Dsi [m] | 0.015748 |  |  |  | 
T0 [C] | 69.47 |  | Deo [m] | 0.0445 |  | Pr_ei | 0.695 |  | Dso [m] | 0.018288 |  |  |  | 
TLe_guess [C] | 65.77 |  | rei [m] | 0.0207 |  | Re_ei | 25526 |  | rsi [m] | 0.007874 |  |  |  | 
TmLe_guess [C] | 100.57 |  | reo [m] | 0.0222 |  | x_fdhe [m] | 0.41 |  | rso [m] | 0.009144 |  |  |  | 
Tmie [C] | 99.87 |  | Le [m] | 0.3000 |  | x_fdte [m] | 0.41 |  | ks [W/(m-K)] | 25 |  |  |  | 
TLs_guess [C] | 21.33 |  | ke [W/(m-K)] | 25 |  | f | 0.02459455 |  | m [m^-2] | 18.3520 |  |  |  | 
ue [ft/min/10] | 284.67 |  |  |  |  | Nuei | 61.7713 |  | Ls [m] | 0.187325 |  |  |  | 
 |  |  |  |  |  | C_nozzle | 2.4254 |  |  |  |  | Key |  | 
 |  |  | Exhaust Pipe Outside Air |  |  | m_nozzle | 0.676 |  | Sensor Pipe Outside Air |  |  |  | Film Temperature | 
 |  |  | TLe_guess [K] | 338.77 |  | Nuei_bar | 101.0616 |  | Tfs [K] | 304.28 |  |  |  | 
 |  |  | Tfe [K] | 316.31 |  | hei [W/(m^2-K)] | 77.58 |  | beta_s [K^-1] | 3.29E-03 |  |  | Convection Coefficient | 
 |  |  | beta_e [K^-1] | 3.16E-03 |  |  |  |  | nu_s [m^2/s] | 1.63E-05 |  |  |  | 
 |  |  | nu_e [m^2/s] | 1.75E-05 |  | Exhaust Pipe Temperature Profile |  |  | Pr_s | 0.706 |  |  | Calculated Temperature | 
 |  |  | Pr_e | 0.705 |  | Tmie [K] | 372.87 |  | kinf_s [W/(m-K)] | 2.66E-02 |  |  |  | 
 |  |  | kinf_e [W/(m-K)] | 2.75E-02 |  | Pe [Pa] | 88000 |  | cp_s [J/(kg-K)] | 1007 |  |  |  | 
 |  |  | cp_e [J/(kg-K)] | 1008 |  | R_air [J/(kg-K)] | 286.5 |  |  |  |  |  |  | 
 |  |  |  |  |  | U_bare | 9.4838 |  |  |  |  |  |  | 
 |  |  | Exhaust Pipe Convection/Radiation |  |  | rhoe [kg/m^3] | 0.8238 |  | Sensor Pipe Convection/Radiation |  |  |  |  | 
 |  |  | Gre | 431157 |  | ue [m/s] | 14.4611 |  | Grs | 18214 |  |  |  | 
 |  |  | Rae | 303966 |  | mdote [kg/s] | 0.0161 |  | Ras | 12859 |  |  |  | 
 |  |  | Nue | 10.4521 |  | TmLe [K] | 371.04 |  | Nus | 4.6414 |  |  |  | 
 |  |  | heo_bar [W/(m^2-K)] | 6.4664 |  |  |  |  | hso_bar [W/(m^2-K)] | 6.7509 |  |  |  | 
 |  |  | sigma | 5.67E-08 |  | Exhaust Pipe External Temperature |  |  | sigma | 5.67E-08 |  |  |  | 
 |  |  | epsilon_e | 0.5 |  | Rconv_ie [K/W] | 0.3301 |  | epsilon_s | 0.5 |  |  |  | 
 |  |  | hr_avge [W/(m^2-K)] | 3.6100 |  | Rconde [K/W] | 0.0015 |  | hr_avgs [W/(m^2-K)] | 3.1998 |  |  |  | 
 |  |  | heo [W/(m^2-K)] | 10.08 |  | Rconv_oe [K/W] | 2.3686 |  | hso [W/(m^2-K)] | 9.95 |  |  |  | 
 |  |  |  |  |  | qe [W] | 29.2724 |  |  |  |  |  |  | 
 |  |  |  |  |  | TLe [K] | 361.34 |  | TLs [K] | 296.45 |  |  |  | 
Excel sheet used to perform calculations.
Predicted plot of sensor pipe temperature vs. length with measured values shown. Bars on measured results represent 95% confidence.
Calculations and Results
Chart: Temperature Profile through Sensor Pipe
| 0 | 0.01 | 0.02 | 0.03 | 0.04 | 0.05 | 0.06 | 7.0000000000000007E-2 | 0.08 | 0.09 | 0.1 | 0.11 | 0.12 | 0.13 | 0.14000000000000001 | 0.15 | 0.16 | 0.17 | 0.18 | 0.18732499999999999 | 0.19
Predicted Results | 86.864 | 85.7605 | 82.6221 | 77.9033 | 72.1943 | 66.0691 | 59.9858 | 54.2541 | 49.0482 | 44.4404 | 40.4352 | 36.9979 | 34.0743 | 31.6034 | 29.5242 | 27.7802 | 26.3205 | 25.1007 | 24.0825 | 23.4455 | 23.2332
Measured Results | 65.77
Measured Results (TLs) | 21.3333

## Slide 6: Discussion of Results and Conclusions
Challenges
Test conditions not controlled as well as hoped. Assumed quiescent air, had forced convection at times.
Largest error likely from predicting TLe
  Thermal circuit models whole length of pipe instead of just end
  Cold forced convection in test area caused lower temp readings
  Instrument error, infrared vs. thermocouple
Imagine the size of the weld bead before we ground it.
Conclusions
Heat transfer is Fun!
With appropriate assumptions and simplifications modeling method can still be fairly accurate
Use a metal with low conductance so the heat transfer is less through the sensor pipe
Weld size and type can act as heat sink