## Slide 1: Hot dogs, HOT Dogs, and more hot dogs…
Me 340: Heat Transfer
Spencer Madsen
Dan Shelley

## Slide 2: Time To Cook a Hot Dog
Me 340: Heat Transfer
Spencer Madsen
Dan Shelley

## Slide 3: The Problem
We love hot dogs!
We wanted to know how long it would take to cook a hot dog to a certain temperature
Through experimental results we chose 80° C for the desired inside temperature.
The goal was to create a mathematical model that could be validated by empirical results.

## Slide 4: Our Assumptions
Temperature of the boiling water was 100° C
The hot dog can be analyzed as an infinite cylinder
The hot dog has constant properties
The hot dog’s properties are:
  k = .52 W/m-K
  ρ = 880 kg/m3
  cp = 3350 J/kg-K
  h = 100 W/m2-K
  r0 = 10 mm or .01 m
  Ti = 6° C
  T∞ = 100° C
  Tf = 80° C

## Slide 5: The Experiment
First:
  We cooked a hot dog in boiling water until it was done. Once done we measured the inside temperature with a thermometer. Tf = 80° C
Second:
  We performed the analysis to calculate the time.
Third:
  We performed the experiment again, measured the time, and measured the outside temperature.

## Slide 6: The Analysis
First:
  Found the Biot Number
    Bi = hLc/k = hr0/2k = (100 W/m2-K *(.01 m))/(2*(.52) W/m-K)
    Bi = .96
  Since Bi > .1 Analysis with lumped capacitance is inappropriate.
Second:
  Therefore, we used the Heisler Chart
    Bi = hr0/k = (100 W/m2-K *(.01 m))/(.52 W/m-K)
    Bi = 1.92
  Found Θ0* = Θ0/Θi = (Tf-T∞)/(Ti-T∞)
    Θ0* = (80-100)/(6-100) = .21

## Slide 7: The Analysis
Third:
  Found Fo = t* where t* = αt/r02 Therefore, Fo = .8
    Also α = k/(ρcp) = (.52 W/m-K)/((880 kg/m3)*(3350 J/kg-K))
    α = 1.764E-7 m2/s
Finally:
  So t = (r02Fo)/α = ((.01 m)2(.8))/(1.764E-7 m2/s)
  t = 453.5 seconds or 7.6 minutes

## Slide 8: Conclusion
Analytical
Experimental
Time calculated to cook a hot dog to 80° C was 7.6 minutes
Time to actually cook a hot dog to 80° C was 6.2 minutes

## Slide 9: Discussion
Reasons why our analysis and experimental results differed:
  Thermometer’s time constant and inaccuracy
  Boiling temperature differs with altitude
  Each hot dog differs slightly in properties
  Human error in the experimental design