## Slide 1: Power Output of a Rear Defrost Car Window
By Allan Peaden & Nick Wasley
Winter 2010

## Slide 2: Problem
Find the power output of a rear defrost window of a car through temperature measurements and calculations.

## Slide 3: Window to be measured
Measuring Device-Infrared Thermometer

## Slide 4: Gathered Data
Air Temperature = 38 deg. Fahrenheit
Wind Speed ≈ 5 MPH
Glass Thickness = 5mm
Glass Dimensions = 47 X 22 inches
Emissivity of glass = 0.92
Angle of Back Window ≈ 60 degrees
Average voltage output from car battery ≤ 12V
Fuse Rating ≤ 20 amps

## Slide 5: Temperature Readings
Time (sec) | Temperature (Celsius)
0 | 3.61
15 | 4.78
30 | 6.00
45 | 7.22
60 | 6.78
75 | 8.17
90 | 9.78
105 | 11.17
120 | 11.44
135 | 11.44
150 | 13.50
165 | 12.89
180 | 11.17
195 | 12.28
210 | 12.17
Chart: Infrared Temperature Readings
| 0 | 15 | 30 | 45 | 60 | 75 | 90 | 105 | 120 | 135 | 150 | 165 | 180 | 195 | 210
Temperature | 3.6111 | 4.7778 | 6 | 7.2222 | 6.7778 | 8.1667 | 9.7778 | 11.1667 | 11.4444 | 11.4444 | 13.5 | 12.8889 | 11.1667 | 12.2778 | 12.1667

## Slide 6: Assumptions
Conduction Neglected
Even temperature distribution in glass
Lumped Capacitance
Constant wind speed & air temperature
Steady-state surface temperature ≈ 285.3 Kelvin

## Slide 7: Equations
EIN = EOUT
Eout = convout + convin + radiation
Eout = hout Aout(Ts - T∞) + hin Ain(Ts - T∞) + 2Aεσ(Ts4 - Tsur4)

## Slide 8: Calculations
hin = 2.639
Nufree = 73.23
Nuforce = 257
Nu7/2 = Nuforce7/2 + Nufree7/2
hout = 5.34
Eout = 103.94 watts

## Slide 9: Conclusion
Power output of rear defrost was found to be 104 watts.
Assuming a 12V output and a current of under 12 amps, this answer seems reasonable. (I = P/V or I = 104/12 = 8.7 amps)